## Slide 1: Draft for a 70 Million European Photovoltaic Building Program
Facts and Data
Ralf Preu, Lorenz Friedrich, Sebastian Nold, Jochen Rentsch, Thomas Schlegl, Andreas Bett
www.ise.fraunhofer.de

## Slide 2: Overview and Disclaimer
Objective and Approach
Renewable Energy Production
GHG Emissions – Impact on the EU Climate Goals
Economic and Employment Effects – Installations and Manufacturing
Disclaimer:
The following analysis of economical and environmental benefits is based on a very simple model, which presumes 70 Mio Buildings in the EU-27 to be available to implement photovoltaics, a number which was postulated and not reconfirmed. A scientifically sound and publishable deduction would demand a more comprehensive approach.

## Slide 3: 70 Million Buildings Program Objective and Approach
Objective:
  The objective of this analysis is to get an idea of potential political statements which could be used to support a program which incentifies to equip 70 Mio. buildings in the EU-27 with photovoltaic systems. These number are not validated for external use yet and must be confirmed scientifically before publishing.
Simplified Approach:
The approach is based on a postulated number of 70 Mio buildings in the EU-27 with photovoltaic buildings an average nominal system power of 15 kWp, an average specific yield of the EU-27 in 2018 of 1,13 kWh/Wp, an invest incentive of 20% and average personnel cost of 50 k€/person and year. Green house gas mitigation values are calculated on a thorough approach based on the ecoinvent database, which will be published soon. For the employment impact it is further assumed that the whole added value is generated in the EU-27, the share of direct labor is estimated to 8%. The share of added value of module technology for residential application is estimated at around 30%.

## Slide 4: 70 Million Buildings Program Renewable Energy Production
70 Million PV systems to be installed in the period 2021-2030
Average PV power 15 kWp/system
Final installed PV power: 1.05 TWp
Specific energy yield: 1.13 kWh/Wp
Annually generated electricity at the end of program : 1,184 TWh/a

## Slide 5: 70 Million Buildings Program GHG Emissions – Impact on the EU Climate Goals
Today GHG-emission of EU-27 energy mix: 404 g CO2-eq/kWh
GHG-emission PV: 28,1 g CO2-eq/kWh (30 a PV system lifetime, irradiation: 1173 kWh/m²a)
Annually saved GHG-potential by initiative at end of initiative: 445 Mt CO2-eq/a
  For comparision: total GHG emissions in EU-27 in 2017: 3977,72 Mt CO2-eq/a
  In 2030 savings of total GHG emissions compared to 2017: 11%

## Slide 6: 70 Million Buildings Program Economic and Employment Effects – Installations and Manufacturing
Average price for PV related to building: 1000 €/kWp
Total Investment for 70 Mio building program: 1,045 Mrd€
Duration of investment program: 10 a; Invest related relative incentive: 20%
Average EU annual investment for 70 Mio building program: 20.9 Mrd€/a
Ratio of GDP EU-27: 0,16%
Total annual cost per capita: 46,87 €/person/a
Total employment program: 21 Mio. person-years
Average annual employment: 2.1 Mio. EU citizens
Added value share for PV module manufacturing: 30%
Direct labor in PV manufacturing: approx. 50,000

## Slide 7: References
Technical Potential
“Technical potential for photovoltaics on buildings in the EU-27”, P.R. Defaix, W.G.J.H.M. van Sark E. Worrell, E. de Visser, Solar Energy 86 (2012) 2644–2653
Energy data and greenhouse effect
https://ec.europa.eu/energy/data-analysis/energy-statistical-pocketbook_en#eu-energy-in-figures energy_statistical_countrydatasheets (1).xlsx
Socio-economic benefits
IRENA (2017), Renewable energy benefits: Leveraging local capacity for solar PV, International Renewable Energy Agency, Abu Dhabi, https://www.irena.org/publications/2017/Jun/Renewable-Energy-Benefits-Leveraging-Local-Capacity-for-Solar-PV

## Slide 8: Annex: Calculation
EU-27 data | Unit | Value_2018 | Source | Remark
Number of buildings in EU | 1000 | 107.500 |  | Ich habe nur eine Zahl von 215 Mio. Wohnungen in der EU gefunden. Weder eine belastbare Zahl für Gebäude in EU und noch nicht mal in D.
Number of building in EU to be equipped with PV | 1000 | 70.000 | Bloss/Fridays for Future ? | 
Ratio of buildings to be equipped with PV |  | 65% |  | 
Number of PV systems in Europe |  | 3.400 |  | Annahme: 1700000 Gebäude.Systeme in Deutschland machen ca. die Hälfte der installierten Leistung
Share of PV Systems in Europe related to buildings |  | 95% |  | 
PV Systems in Europe in buildings | 1000 | 3230 |  | 
Share of installed PV power related to buildings |  | 50% |  | 
Installed PV Power | GW | 102 | https://ec.europa.eu/energy/data-analysis/energy-statistical-pocketbook_en#eu-energy-in-figures energy_statistical_countrydatasheets (1).xlsx | 
Average PV power of PV buildings in EU | kW | 14,9 |  | grobe Schätzung, 1.700.000 PV-Systeme in D, 95% buildings, ca. 50% der gesamten Kapazität (d.h.50/2 GWp), d.h. 25 GWp mit 1,63 Mio. Gebäuden macht 15 kWp/Gebäude. Leider habe ich hierfür weder Daten für EU noch für D gefunden.
Capacity to be installed after program | GW | 1045 |  | 
Annual Electricity PV | TWh/a | 114,98 | https://ec.europa.eu/energy/data-analysis/energy-statistical-pocketbook_en#eu-energy-in-figures energy_statistical_countrydatasheets (1).xlsx | evtl. 2% Solar Thermal Electricity included
Average specific yield | kWh/Wp | 1,13 |  | 
Annual electricity PV after program | TWh/a | 1.183,62 |  | 
GHG-emission EU-27 low voltage | g CO2-eq/kWh | 404 |  | Teameintrag Lorenz Friedrich: Strom- Mix Niederspannung EU-27_2020: 404 g CO2-eq/kWh Strom- Mix Mittelspannung EU-27_2020: 401 g CO2-eq/kWh Vorgehen FYI: Mit Umberto Software aus den Ecoinvent Datensätzen "Market group for electricity" die "market for electricity" Datensätze aller Nicht EU Länder entfernt, Anteile der verbliebenen Länder neu skaliert auf den Output "1 kWh" und mit IPCC GWP 100 a das Treibhausgaspotential errechnet.
GHG-emission by PV produced in EU-27 | g CO2-eq/kWh | 28,1 |  | Teameintrag Lorenz Friedrich: EU 20% Wirkungsgrad 28,1 g CO2-eq/kWh Vorgehen FYI: Mit Umberto Software aus den Ecoinvent Datensätzen "Market group for electricity" die "market for e
Annually saved GHG-potential by initative at end of period | Mt CO2-eq/a | 445 |  | 
Total GHG emissions in EU-27 in 2017 | Mt CO2-eq/a | 3977,72 | https://ec.europa.eu/energy/data-analysis/energy-statistical-pocketbook_en#eu-energy-in-figures energy_statistical_countrydatasheets (1).xlsx | 2017er Wert
Savings of 2017 emissions |  | 11% |  | 
Average price for PV related to building | €/kWp | 1000 | Geschätzter Wert 70MBuilding-Team | 
Total Investment for 70MBuild program | Mrd€ | 1.045,47 |  | 
Duration of investment program | a | 10 | 2021-2030 | 
Invest related relative incentive |  | 20% | Annahme 70MBuilding-Team | 
Average EU annual investment for 70 Mbuild Program | Mrd€/a | 20,91 |  | 
Ratio of GDP EU-27 |  | 0,16% |  | 
Total annual cost per capita | €/person/a | 46,87 |  | 
Average personnel cost for person and year | €/person/a | 50.000 | estimated | 
Total employment | 1000 person years | 20.909 |  | 
Average employment | 1000 persons | 2091 |  | 
Added value share for PV module manufacturing |  | 30% | estimated (approximate status for residential in 2020) | 
Average employment PV module manufacturing | 1000 persons | 627,3 |  | 
Share of direct labor in total added value of manufacturing |  | 8% | geschätzt: VDMA-Studie Deutschland 18,4% (!), Polen mit ca. 1/3 der Kosten. | 
Direct Labor in PV manufacturing | 1000 persons | 50,18 |  | 
total population | 1000 | 446098 | https://ec.europa.eu/energy/data-analysis/energy-statistical-pocketbook_en#eu-energy-in-figures energy_statistical_countrydatasheets (1).xlsx | 
Gross Domestic Product-market prices at current prices | Mrd€/a | 13482,1 | https://ec.europa.eu/energy/data-analysis/energy-statistical-pocketbook_en#eu-energy-in-figures energy_statistical_countrydatasheets (1).xlsx |